## Slide 1
SMART BLIND CANE
ROBOTICS PROJECT

## Slide 2
TEAM MEMBERS -
    NILOY SARKAR
    ARIYAN RAHMAN MUGDHO
    MOUTASIM FUAD IFTI

## Slide 3
PROJECT OBJECTIVE
Enhance mobility and safety to visually impared individuals
Providing:
    Obstacle Detection
    Real-time location awareness
    SOS Emergency System

## Slide 4
KEY FEATURES
Obstacle detection with directonal alert
GPS- based tracking system
SOS button to send emergency SMS with coordinates

## Slide 5
HARDWARE COMPONENTS
    Arduino Uno R3
    HC-SR04 Ultrasonic Sensor
    NEO-7M GPS Module
    SIM800L GSM Module
    SG90 Servo Motor
    DC Vibration Motor, Buzzer
    Batteries, Breadboard, Blind Stick

## Slide 6
OBSTACLE DETECTION FUNCTIONALITY
    Servo rotates sensor 0°–180° continuously
    Object within 30 cm triggers buzzer
    Beep frequency changes by direction:
      800 Hz = Left
      1200 Hz = Right
    Real-time auditory feedback for navigation

## Slide 7
GPS TRACKING
    5-second GPS data collection
    Provides latitude & longitude
    Displays clickable Google Maps URL
    Works offline via satellite signals

## Slide 8
SOS EMERGENCY ALERT
    Pressing button triggers:
    LED indicator
    GPS coordinate retrieval
    SMS to pre-configured contact
    Sends text + Google Maps link
    Works even in 2G network areas

## Slide 9
CONCLUSION
    Cost-effective assistive tech for the blind
    Increases independence & safety
    Scalable and upgradeable for future versions
    Total cost: 3920 BDT – highly affordable

## Slide 10
THANK YOU